## Slide 1
1
THE CHANGE
Design targets, not yet measured on the robot
One Thing At A Time, Or All At Once
Last season the robot finished one job before starting the next. Now the arm moves while the robot is still driving - and it never stops checking where it is.
0s
1s
2s
3s
4s
Driving
Arm / turret
Frozen
LAST SEASON - wait for each job to finish; the robot stops tracking itself
wheels
Drive to goal
Drive back
arm + aim
Raise arm
Waits
Total 4.0 seconds - and the tracker was frozen for 2.5 s of it.
THIS SEASON - IVY + PEDRO PATHING: jobs overlap; the tracker never stops
wheels
Drive to goal
Drive back
arm + aim
Raise arm
Retract
Total 2.1 seconds - same jobs, same speeds, simply overlapped.
1.9×
faster scoring cycle
4.0 s → 2.1 s
50×
fresher aiming data
300 ms old → 6 ms
45×
tighter aim at speed
~45 cm → under 1 cm
60×
quicker sensor reads
20 ms → 0.3 ms a pass
1 / 4

## Slide 2
2
WHAT WE ACTUALLY BUILD
The Pieces To Write
Nine files carry the design. Once Lift exists, every other mechanism is the same shape.
Robot
CONDUCTOR
Runs the six-step pass and keeps the list of mechanisms.
- startCycle() / read() / write()
- holds every subsystem
Subsystem
THE MOULD
The shape every mechanism must fit. Four methods.
- read() - look at hardware
- write() - move hardware
Drive
WHEELS
Wraps Pedro, and claims the drivetrain so paths can't fight.
- follow(path) / turnTo(angle)
- waitForT(0.55) - 55% along
Lift
PATTERN
The template for every mechanism. Commands only set a target.
- goTo(HIGH) - with a timeout
- position / target
Turret
AIMING
Aims all match, and steps aside when a job needs it fixed.
- trackGoal() - never-ending
- holdAt(angle) - takes over
Vision
LIMELIGHT 3A
Collects the answer the smart camera already worked out.
- hasFix() / fieldPose()
- drops sightings over 100 ms
Paths
MAP
Every curve we will drive, worked out before the match.
- startToScore, park, and so on
- built once, at start-up
Routines
GAME PLAN
The recipes: what runs together, and what runs in order.
- scoreCycle() / intakeCycle()
- every step has a time limit
LoopTimer
STOPWATCH
Shows typical and worst pass time, so a stall is obvious.
- median / p95 / worst
- target 6 ms, worst 12 ms
2 / 4

## Slide 3
3
HOW IT FITS TOGETHER
we write it
Pedro / Ivy
FTC SDK
The Modules We Will Build
Every box is a class. Arrows show what creates or calls what. Colour shows who wrote it.
AutoBlueLeft AutoRedRight BiobuzzTeleOp
extends LinearOpMode - owns nothing, runs the loop
Paths
PathChains, built at init
Routines
the game-plan recipes
Scheduler (Ivy)
Command / Groups / Pedro
OpMode builds these at init
Robot - startCycle() / read() / follower.update() / Scheduler.execute() / write()
Drive
wheels + paths
Lift
the arm
Turret
aiming
Intake
grabbing
Vision
the camera
.requiring(...) - one owner at a time
Follower
Pedro Pathing
DcMotorEx / Servo
FTC SDK
Limelight3A
FTC SDK - own processor
write()
read()
UTILITIES
Fork
run a job alongside
Timeouts
every wait must end
LoopTimer
median / p95 / worst
PoseBuffer
where we were, when
AimSolver
pure aiming maths
3 / 4

## Slide 4
4
THE PART EVERYONE ASKS ABOUT
How Ivy's Scheduler Works
Ivy is not doing several things at the same instant. It does one thing at a time, extremely fast, switching about 165 times a second - which looks identical from the stands.
1
Grab every sensor reading in one go
0.3 ms
2
Copy those readings into memory
~0 ms
3
Pedro updates where we are and steers
0.5 ms
4
Ivy runs - every job gets one quick turn
0.1 ms
5
Send out only the values that changed
0-4 ms
6
Update the driver screen, 10× a second
~0 ms
repeat - about 165 times a second
Step 4: Ivy walks its list and gives each job one turn - a tiny bit of work, then "am I finished?"
[ follow path - working ] [ raise arm - working ]
[ aim turret - never ends ] [ grab - finished ]
Is it multithreaded?
No - one thread, one job at a time.
The camera is its own computer, not a thread.
Then how do things happen at once?
While the arm rises, it gets ~200 turns.
What breaks it?
A job that stops and waits freezes all.
Camera setup calls can wait 15 seconds.
Who wins if two jobs want the arm?
The higher-priority job. The other resumes.
What if something goes wrong mid-match?
Every job has a time limit. Auto: 28 s.
Full detail: docs/architecture/autonomous-command-architecture.md / pedropathing.com/docs/ivy
4 / 4